DISCLAIMER

         These docs were graciously translated from German to English
         by Mike, WB0UPX, and were transcribed by me from hardcopy to
         disk. Great care has been taken to preserve the meaning and
         accuracy contained therein. I did however take the liberty to
         correct some spelling and punctuation errors.

         We make no guarantee as to the origial accuracy of these doc.
         We also do not claim responsibility for problems encountered
         with the Graphic Packet program.

         Please address comments or questions about GP to its author,
         DH1DAE.

         We congratulate DH1DAE for a fine packet program. 73 and
         enjoy, Tom, KA4P


















































                             GRAPHIC PACKET V 1.00

         1. General information:

         GP is a terminal program that utilizes Host-mode software
         such as WA8DED or "The Firmware". Other TNC software may be
         used, provided the software supports KISS mode operation.

         GP differs from other terminal software in that it uses
         graphics and is very easy to use. For all important
         functions, icons are built into the program and operate with
         a mouse. If a mouse is not present, the icons can be called
         through definition of hot keys.

         GP offers a maximum of 10 channels, the total number being at
         the discretion of the user.

         For mailbox operation, there is a checklist (called through
         the "(C)heck" command) which is held in a special buffer.
         From this list the user can select specific text. The same
         applies for the command "(L)ist".

         There is also a small text editor built into GP to allow
         editing of text files, in particular the configuration files.

         System requirements for GP are an IBM compatible computer
         with a minimum of 512K, EGA/VGA graphics card, and DOS 2.0 or
         later version. If the computer has extended memory installed,
         GP will use the EMS area for the scroll-back buffer and only
         275K of lower RAM is required.

         1.1 The difference between GP.EXE and GP286.EXE

         GP is compiled in two different versions to allow for
         different processor types.

         GP.EXE will run on all processors of the 80x86 family, as
         well as the 8088, 8086, 80286, etc.

         GP286.EXE supports the additional commands of the 80286 and
         is therefore not compatible with the 8086/8088 series
         processors.

         In operation GP286.EXE and GP.EXE are identical. (GP286.EXE
         has run on some XT's that have the NEC V20 processor
         installed).

         1.2 Updates

         Anyone interested in the newest version of GP can send a
         blank diskette and sufficient postage cost to the following
         address:


                                    Page 1










         Ulf Saren
         DH1DAE
         Veit-Stoa-Strasse 36
         5900 Seigen
         Germany

         Should the GP program impress you, and you become a steady
         user, please send a short message to DH1DAE @ DB0SGL.DE.EU
         giving a short description of your system configuration.
         Particularly interesting would be the following points:

         How much RAM does your PC have?
         Are you using and EMS configuration - if yes, how much?
         Which graphic card is installed in your system?
         Which DOS version are you using?

         1.3 Questions and recommendations

         Anyone with questions or problems pertaining to GP can send a
         short message to DH1DAE @ DB0SGL. The same applies for any
         recommendations for future releases.

         1.4 Copyrights

         GP is placed in the public domain and may be freely copied
         and distributed to third parties, provided no fee or costs
         are charged and complete documentation accompanies the
         program. Commercial use and distribution is not allowed.

         GP may be used by all licensed amateur radio operators to the
         extent allowed by their class of license. SWL's may also use
         GP to copy packet radio contacts.

         The author of GP issues no guarantee with the use of the
         program and assumes no responsibility for loss of or damage
         to equipment, files, or data.

         It is up to each user as to whether he would like to make a
         donation to the author for this release or for the
         development of future releases. Keep in mind that the
         development of this program as well as future releases
         requires a significant investment in time and work. If you
         feel the program is of value to you, then invest a small
         donation to allow work to continue.

         2. Installation

         GP may be run from a floppy diskette but with the constant
         disk access required, will be very slow in comparison to
         installation on a hard disk.

         To install GP on a hard disk, simply make the appropriate



                                    Page 2










         subdirectory on the hard disk and copy all files from the
         floppy to this subdirectory. For remote operations you will
         require and additional subdirectory (named as you please).
         The path to this subdirectory must be placed in your
         configuration data.
         To implement the command "//RUN" a second subdirectory must
         be made. This command allows you to call and run a secondary
         program which may be sent to the calling station. For this
         reason the second subdirectory may not be under the GP
         directory. Since GP is also an external program, it would be
         possible to call and run it remotely, causing severe
         complications. The commands for the configuration data are
         defined in para 3.1. The files DH1DAE.* are given as examples
         as different functions of GP and should be used for
         information purposes only. These files should not be
         installed on the hard disk. In addition, the files F1.GPI and
         F&.GPI are examples of the only permanent text files which
         may be called up using the Shift-F1...Shift-F10 function
         keys.

         2.1 Installation examples

         To use GP, the following files are required:

         GP.EXE or GP286.EXE      (Self extracting)
         BINDATA.GP               (Data for Windows)
         ICONS.GP                 (Data for symbols)
         CONFIG.GP                (Configuration file)
         HELP.EXE                 (Remote operation help manager)

         The remainder of the files are not necessarily required to
         use GP. The files CTEXT.GPI and QRT.GPI allow the user to
         define permanent text for connect and disconnect messages. In
         the file NAMES.GPI, the names and paths of various stations
         that have used command "//NAME" are automatically stored.
         This information may also be entered manually. If a station
         exists in the list, you need only type the station callsign
         when trying to connect. GP extracts the path data
         automatically from this file.

         EXAMPLE:

          - GP is installed on a hard disk under the subdirectory
         "C:\GP"
          - All control functions should be placed in the subdirectory
         "C:\GP\USER.GP
          - All programs that you would allow to be run by remote
         operators should be placed in the subdirectory
         "C:\GP\EXTERNAL.GP
          - The storage of text files should be placed in the
         subdirectory "C:\GP\SAVE.GP
          - The original diskette with GP should be placed in drive A.



                                    Page 3










         Step by step installation would then be as follows:

         C:\ md gp

         C:\ cd gp

         C:\GP>copy a:\gp.exe (NOTE: or gp286.exe)
                1 file copied

         C:\GP>copy a:\icons.gp
                1 files copied

         C:\GP>copy a:\config.gp
                1 files copied

         C:\GP>copy a:\help.exe
                1 files copied

         C:\GP>copy a:\ctext.gpi
                1 files copied

         C:\GP>copy a:\qrt.gpi
                1 files copied

         C:\GP>md external.gp

         C:\GP>md user.gp

         C:\GP>md save.gp

         C:\GP>copy a:\external.gp\sysinfo.exe external.gp

         C:\GP>

         You must now make changes in the CONFIG.GP file, particularly
         in the path for control commands and saving of text.

         UserDir = C:\GP\USER.GP
         ExternalDir = C:\GP\EXTERNAL.GP
         SaveDir = C:\GP\SAVE.GP
         LogDir = C:\GP

         You must also enter your own callsign

         MYCALL - ??????

         As received, the GP MYCALL value is NOCALL.

         The data for the serial port is set at a default value of
         9600 and com1. Should the TNC be connected to another com
         port or should you require a different baud rate, you must
         change the "SerBaud" and "SerNr" parameters for your system.
         Should you desire to connect GP to a third or


                                    Page 4










         fourth serial port, you will have to change not only the port
         number, but also the IRQ (interrupt). Check your users guide
         for your serial port for the correct interrupt.

         At this time you should enter the data for NAMES.GP by giving
         the callsign, name, and path to the stations which you often
         connect to. The syntax for this information can be found
         under Para 3.6 as well as examples under NAMES.GP in the
         original diskette.

         3. SUPPORTING INFORMATION

         3.1 Configuration data

         All of the necessary parameters for GP are found in the file
         CONFIG.GP. The parameters must be configured before starting
         GP for the first time, particularly those dealing with the
         serial port, the display driver, and the remote operations
         path, The syntax for all variables is the same,
         "Variable = Value", ie "Zoom = 2". Comments may also be
         entered by use of a semicolon. Example:
         "Zoom = 2   ;  Set the value of Zoom to 2".

         3.1.1   Color

         The screen display of GP is divided into various windows.
         Each window may be displayed in a different color at the
         discretion of the user. The following color choices are
         available:
         Black
         Blue
         Green
         Cyan
         Red
         Magenta
         Orange
         LightGray
         DarkGray
         LightBlue
         LightGreen
         LightCyan
         LightRed
         LightMagenta
         Yellow
         White

         The following system variables control colors as indicated:

         MonitorBackGround   : Background color for monitor window
         MonitorForeGround   : Text color for monitor window
                               (Information packets)




                                    Page 5










         MonitorInversAttr   :  Text color for monitor window
                                (Packet header info)
         EditorBackGround    :  Background color for editor window
         EditorForeGround    :  Text color for editor window
         CheckBackGround     :  Background color for check window
         CheckForeGround     :  Text color
         CheckInversAttr     :  Border and marked data color
         ConnectBackGround   :  Background color of connect windows
                                (Channels 1 - 10)
         ConnectForeGround   :  Text color of received text
         ConnectInversAttr   :  Text color of sent text
         MenuBackGround      :  Background color of upper menu
         MenuForeGround      :  Text color of upper menu list
         MenuInversAttr      :  Text color of a channel number,
                                other than the active channel, that
                                has unread information.
         StateBackGround     :  Background of the status window
         StateForeGround     :  Text color of status window
         InputBackGround     :  Background of input window
         InputForeGround     :  Text color of input window


         3.1.2  Scroll back buffer

         GP reserves buffer space for each channel to allow for
         scrolling back through the data that has scrolled off the
         screen. The size of the text buffer is set by the user. The
         buffer size is set by number of lines (each line containing
         82 bytes - 80 byte line + 2 bytes for color). The number of
         lines can be between 40 and 795. 40 is the minimum number
         since each screen will show 40 lines and 795 is the maximum
         due to the 8086 limitations of 64KB per storage segment.
         Hence, 795 lines = approx 64K of RAM for scrollback.

         CheckBuffer              :Buffer size for check window
         EditBuffer               :Buffer size for the editor
         TextBuffer               :Buffer size for the monitor as
                                   well as each channel. Entries
                                   must be separated by a comma -
                                   ie Monitor, Channel 1, Channel
                                   2, Channel 3 etc for as many
                                   channels as selected in the initial
                                   configuration (max 10).

         3.1.3   Timer settings

         GP has a screen saver function which blanks the screen after
         a specified amount of time has elapsed since a key was struck
         or since a new line of text has been displayed. The command
         to utilize this feature is "Screensave" and the value
         assigned to this command will be in minutes, ie "Screensave =
         5" means the screen will blank



                                    Page 6










         after 5 minutes of no activity. The same applies to how long
         a pop-up menu will be displayed or a connect notification.
         The command for this function is "PopUpTime" but here the
         time is given in seconds, ie "PopUpTime = 5" would display
         the menu or the connect notification for 5 seconds and then
         clear. Additionally the internal clock of GP is also
         adjustable. Normally it uses the time set by the computer and
         you will find the time and zone displayed in the middle of
         the display field. The command "Time" defines the internal
         time used by GP. The command "Time = -60" would allow the GP
         clock to run 60 minutes behind the computer clock. The
         command "Zone" is used with macro "%z", which displays the
         time zone.

         For automatic logging, it is recommended that UTC time be
         used. This is accomplished with the command "UTC". This is
         done through the use of the command "UTC = -120", where the
         numerical value is the number of minutes your location is
         ahead or behind (+ or -) Greenwich Mean Time.

         The command "ConnectBell" allows for an audible tone when you
         are connected to by another station and how often the bell
         rings. GP emulates a telephone in this case and issues a 3
         tone bell. "ConnectBell - 5" would cause the bell to ring 5
         times.

         3.1.4  Configuring the Serial Port

         GP will work with any configuration of serial port number and
         interrupt (IRQ), to include AT values of 8 - 15. All values
         may be entered in decimal or hexadecimal, but when using hex,
         the number must be preceded by the "$" symbol, ie $3F8.

         The values of databits, stop bits, and parity cannot be
         changed. They are set permanently at the following values
         - 8 databits, 1 stopbit, 0 parity.

         To configure the serial port the following syntax is used:

         SerNr          :  Serial port number
         SerBaud        :  Baud rate for the serial port
         SerPort        :  Address of the serial port - $3F8, $2F8 etc
         SerIrq         :  Interpol number - 3, 4, 5, 6 etc

         3.1.5  Setting the path

         For the commands //Dir, //Write, //Read, and //Delete you
         must establish a path to the directory that these commands
         will access. All stations have the same priority in that they
         may all read from or write to this directory. This is the
         directory that you would want them to have access to and NOT
         to your GP or root directory. The



                                    Page 7










         command to establish the path to this directory is "UserDir".
         Another path should be established to allow implementation of
         the command "//Run". For example on the original program
         diskette, you will find the program "Sysinfo.exe" under the
         directory GP\EXTERNAL.GP. This program can be run from DOS,
         or from within GP with the "//Run" command, and gives
         information about the configuration of your computer. The
         path for use of external programs would be entered with the
         command "ExternalDir = ". The last path is to establish the
         directory where received text that you wish to retain is
         saved. The command to establish this path is "SaveDir".

         The default paths are those that were set up during the
         initial installation of GP in Para 2.1.

         3.1.6 TNC initialization

         At the start of GP, or upon exiting, the TNC may be
         initialized or de-initialized. The syntax for this process is
         always:

         TNCINI - tnc command(s)

         where "tnc command" can be any or all of "The firmware"
         commands. For the de-initialization of the TNC, the syntax is
         identical to that above, except the command
         "TNCDEI = command(s)" is used.

         Should you want to use the DOS shell while operating under
         GP, it is necessary to turn off the monitor function of GP.
         Failure to do so would leave the monitor buffer running and
         would soon fill. To enter the DOS shell from within GP, first
         use the command "TNCDOS = tnc command" with the syntax as
         described above. After exiting from the DOS shell, the TNCINI
         values would be reestablished.

         3.1.7  Printers

         Should you want to transfer a QSO to a printer, you can
         naturally print both the sent and received text from
         different windows, provided your printer allows this. All
         Epson compatible printers offer several possibilities. GP
         allows up to 10 control characters per attribute. Control
         characters must be entered in decimal numbers and separated
         by commas. The command "DefaultPrint" sets the print
         attributes for received text and the command "InversPrint"
         sets the printer attributes for sent text. Refer to your
         printer manual for print attributes.

         3.1.8  Other adjustments

         The establishments of number of channels to use is



                                    Page 8










         accomplished with the command "Channels". The number of
         channels can be from 1 to 10. Remember, however, not to enter
         more channels than the TNC is capable of controlling. It is
         not possible for GP to ascertain the channel capability of
         your TNC. For this reason, it is essential you enter the
         number of channels you feel comfortable with, not to exceed
         your TNC's capabilities. The syntax is as follows:
              Channels = <1......10>   :ie Channels = 4

         The MYCALL command tells the system what callsign to use and
         initializes the TNC with this callsign. It is possible to
         assign a different callsign (SSID) to each channel. A channel
         with no callsign specifically assigned will default to the
         monitor screen. The callsigns are entered in channel-
         sequence, each callsign/channel separated by a comma. As an
         example:
              SYNTAX:  MYCALL = <Monitor>, <Channel 1>, , <Channel 3>
              COMMAND: MYCALL = WB0UPX, WB0UPX-2, , WB0UPX-8

         In this example the monitor callsign would be WB0UPX, the
         callsign for channel 1 would be WB0UPX-2, the callsign for
         channels 2 and 4 would default to WB0UPX since they are
         blank, and channel 3's callsign would be WB0UPX-8.

         The command "Prompt" allows you to define a system prompt
         which, with the proper remote command, also sends the prompt
         to the connected station.

         To allow received packets to be more legible on the monitor
         screen, you may insert a blank line between each received
         line. The command for this is "InsertMonLine On/Off".

         To activate the automatic logging feature, give the command
         "Log On/Off". If the auto logging is turned on, you must
         enter the packet operating frequency. This can be either the
         exact frequency or the operating band, ie 430.625 or 70cm.
         The numeric entry for the frequency can be no longer than 7
         digits. The command for this is "QRG = <Freq>".

         The Backup command makes it possible, upon ending GP, to save
         the text buffers to disk and then reload them the next time
         GP is run. This way, QSO information is not lost, even if a
         contact is broken in the middle of a QSO. The command to
         activate this feature is "Backup On/Off".

         Packets received on a valid channel may be set to give an
         audible signal. This is done with the command "RXClick". The
         values for this command are as follows:

         RXClick = 0    :  No signal
         RXClick = 1    :  Signal on, but not for the active channel
         RXClick = 2    :  Signal on regardless of channel



                                    Page 9










         3.2  *.GPI Files

         The *.GPI stands for Graphic Packet Infofile. Files under
         this heading contain information that may be open, read,
         deleted, etc from other stations through the use of remote
         commands. In all files under this category, it is possible to
         build a place holder for defined macros. There are a total of
         9 macros available for use. The placeholder for each of these
         macros are defined as follows:

         %V : Version number of the software, in this case "1.00"
         %C : Call of the connecting station
         %N : Name of the connecting station
         %Y : Your call
         %K : Channel number from which info will be sent
         %T : Actual GP time in HH:MM:SS format
         %D : Actual date with day, ie Mon, 25.03.1993
         %B : Control character for the bell (07h)
         %I : If the file "NEWS.GPI" is present, it will send the text
              from this file. If not, it is ignored
         %Z : Gives the time zone
         %_ : Forces a carriage return and line feed
         %% : Sends the percent symbol

         It is also possible to define the length of each macro to be
         sent. As an example, the %N-macro. The format to set a fixed
         length is "%N#20". This would establish a 20 character space
         for the name, regardless of the length of the name.

         3.2.1 The file "CTEXT.GPI"
         This file contains the greeting text that is sent to a
         station when it first connects.

         3.2.2 The file "NEWS.GPI"
         This file contains news bulletins of general information. The
         file can be read with the //NEWS command. The text in the
         file can be erased and changed as the situation dictates.

         3.2.3 The file "<MYCALL>.GPI"
         This file is brought up with the command "//INFO". It
         contains a short description of your station. (Brag file).

         3.2.4 The file "F1.GPI"...."F12.GPI"
         These files contain text macros. They are called through the
         Shift+Function key and each file name corresponds with the
         numbered function key. Naturally, F11 and F12 files can only
         be used by your system if these keys exist on your keyboard.








                                    Page 10










         3.2.5 The file "QRT.GPI"
         The text from this file would be sent as soon as the command
         //Q is received from the connected station. As soon as the
         text has been sent, a disconnect would be initiated by your
         station.

         3.2.6 The file "RUN.GPI"
         If your station receives a "//RUN ?" remote command from a
         connected station, the contents of this file would be sent to
         him/her. This file should contain a short description of all
         external programs that can be called up with the "//RUN"
         command.

         3.3 The file "<CALL>.GPC"
         In this file, personal connect-text messages for specific
         stations may be stored. When the addressed station connects,
         he would receive the contents of this file and the normal
         CTEXT file would be ignored. This file, as with *.GPI files,
         can use all of the macros described above.

         3.4 The file "<CALL>.GPM"
         The file extension on this file stands for "Graphic Packet
         Mail". With the help of this file, personal messages may be
         stored and sent to the address <CALL> station. There can only
         be one file per callsign stored at any one time. As with the
         *.GPC file above, the contents of this file would be
         forwarded as soon as the addressed station connected and the
         normal CTEXT file would be ignored. Also all of the macros
         described above may be used in this file.

         3.5 The file "MHEARD.GPI"
         GP maintains internally an MH-list of the last 20 station
         callsigns which may be accessed by any connected station with
         the command "//MH". This list is stored to disk under the
         above name upon closing GP.

         3.6 The file "NAMES.GP"
         This file contains the names and connecting paths of other
         stations. Connecting stations may enter their data into this
         file with the command "//NAME". Since the file is stored in
         ascii-text, the data contained here in can be manually
         entered or changed. For detailed information on the syntax
         for path entry, see para 9.

         3.7 The file "*.GPB"
         The file extension GPB stands for Graphic Packet Backup and
         provides the ability to store the existing file data to disk
         upon closing GP and then restore this information to GP when
         next started. This information should not be tampered with or
         altered. Through the use of Backup, it is possible to leave
         GP and then restart the program during a QSO without
         disconnecting. The file CSTAT.GPB contains the QSO data.



                                    Page 11










         In the file BUFFERS.GPB, all of the buffer text data is
         stored. Also in the CSTAT.GPB file, the control codes for
         each channel and the soft scrolling information is stored.
         This possible only when "Backup = ON".

         3.8 The file "BINDATA.GP"
         This file contains the data for the opening window. Because
         of technical limitations, the opening window cannot be
         displayed in EGA mode.

         3.9 The file "ICONS.GP"
         This file contains all the character information for the icon
         symbols. Icon data will be loaded as required, from floppy or
         hard disk by GP unless you have EMS RAM. If EMS RAM is
         available, then this data will load automatically into RAM
         and is available for GP to use immediately. The icon data
         must be in the same subdirectory as GP. If the ICONS.GP file
         is missing, then only red fields will be displayed where the
         icon would normally appear, but GP will not recognize or
         initiate the intended icon function.

         3.10 The file "<mycall>.GPL"
         The file extension stands for Graphic Packet Logfile and
         contains the logbook information obtained from an integrated
         logbook manager. For each MYCALL there will be a separate
         entry made to allow for a better overview of activities.
         However a separate entry will not be made for each SSID> The
         format for the logbook data is compatible with SP.

         4. Keyboard Commands

         4.1 Keyboard commands applicable to all channels.

         F1...F10       :Turns on channel corresponding to F number
         F11 or Alt-F1  :Check function
         F12 or ALT-F2  :List function
         Alt-M          :Switches to monitor channel
         Alt-E          :Switches to the editor
         Alt-O          :DOS-Shell
         Alt-R          :Soft scroll for designated channel ON/OFF
         Alt-U          :Setup
         Alt-X          :Quit GP program
         Alt-Z          :Zoom ON/OFF (VGA only)
         Alt-F4         :Clear RX window
         Alt-F6         :Shows last link status message
         Alt-F7         :Shows last error message
         <Ins>          :Turns INSERT on or off

         4.2 Keyboard commands for channel 1 ..... 10

         Alt-B          :Scroll border ON/OFF
         Alt-C          :Connect
         Alt-D          :Disconnect


                                    Page 12










         Alt-Y          :Change MYCALL (only while disconnected)
         Alt-S          :Save (Capture to disk)
         Alt-T          :Send a file
         Alt-F8         :Turn split screen ON/OFF
         Alt-F9         :Move division line up (split screen)
         Alt-F10        :Move division line down (split screen)
         SHIFT-F1...F10 :Send text macro #1...10
         Ctrl-D         :Enter date in write ahead buffer
         Ctrl-T         :Enter time in write ahead buffer
         Ctrl-Y         :Erase current line in write ahead buffer
                         (data will be moved to temp buffer and may
                          be recalled with Ctrl-P)
         Ctrl-C         :Copy line from temp buffer (Copy)
         Ctrl-P         :Recall line from temp buffer (Paste)

         4.3 Editor commands

         Alt-L          :Load text
         Alt-S          :Save text
         Ctrl-Y         :Erase line
         Ctrl-C         :Copy line from temp buffer (Copy)
         Ctrl-P         :Recall line from temp buffer (Paste)

         4.4 TheBox check and list commands

         Alt-S          :Sort checklist (does not apply to List)
         cursor keys    :Move marker line to selected option
         <SpaceBar>     :Mark selection
         <Return>       :Send a READ command to mailbox
         <ESC>          :Exit check menu

         4.5 Screen and cursor keys

         Cursor up      :Scrolls back text buffer
         Cursor down    :Scrolls text buffer forward
         Cursor right   :Moves cursor to the right
         Cursor left    :Moves cursor to the left
         Page up        :Scrolls one page back
         Page down      :Scrolls one page forward
         Ctrl-Page up   :Home
         Ctrl-Page down :End
         Ctrl-cursor rt :Moves cursor to start of word to the right
         Ctrl-cursor lt :Moves cursor to start of word to the left
         HOME           :Moves cursor to first line
         END            :Moves cursor to end of line

                             ********************
         NOTE 1: The function Alt-L (load text) and Alt-T (send file)
         require a file name to be given. The use of a wildcard (* or
         ?) in the name will cause the File-Select-Box to appear and
         the designated file can be selected from this box.

         NOTE 2: The HOME and END keys have other functions while in
         the monitor or channel screens. Use of these keys will

                                    Page 13










         move the display window one line up or one line down on the
         screen.

         4.6 ASCII characters 1-31
         Normally you may call up ascii characters 1-31 by use of the
         key combinations of Ctrl-(A...Z). However, certain of the
         ascii functions are already defined by GP. Should it be
         necessary to use a character already defined by GP, the use
         of the Alt-key and the numeric keypad will allow the
         redefinition of the key with numbers from 1-255.

         5. The QSO

         5.1 General information
         GP offers the possibility of conducting up to 10 separate
         QSO's at the same time. There is one channel for each QSO.
         These channels can be called up with the function keys
         F1...F10. Each channel may have its own callsign and this is
         entered with Alt-Y. If you desire to connect to another
         station, you need only to push the function key corresponding
         to a free channel. Once on this channel, simply use the Alt-C
         key and then enter the callsign of the desired station. If
         this station exists in your NAME file, you need not enter the
         path to that station. If the station does not exist in the
         NAME file, then you must enter the callsign of the desired
         station plus any station callsigns that you must digipeat
         through. To end the QSO, simply press the Alt-D keys
         simultaneously. If you have QSO's going on more than one
         channel at the same time, there will be a display (different
         color) for each channel that has received packets that have
         not yet been read. Along with the color change in the upper
         field, you also have the possibility to set an alarm tone
         indicating that unread packets are waiting (see Para 3.1.8).

         Once a connect with another station has been established, you
         simply type your message and press <Enter> to send your
         message. Lines may be edited by use of the cursor keys. The
         text to be sent will be displayed in the upper window. GP
         also allows for word wrap around, in other words, if a word
         at the end of a line is too long to be sent in this packet,
         it will be carried to the next line. This feature allows
         you to simply type and not worry about the length of each
         line prior to transmitting. The default line length for each
         line is 80 characters but this may be changed in the SETUP.
         Practically speaking, you should consider a line length of 65
         characters since the callsigns of both stations appear in the
         sent/received packet. This will keep your text on one line at
         the received station and make reading easier.

         5.2 File transfer (Alt-T)
         This function allows you to send a file from a floppy/hard
         disk to another station. With this function, any defined



                                    Page 14










         macros such as those used by the *.GPI files, are ignored.
         You may transfer three different types of files and these
         are:
         1 - Text files
         2 - Binary files
         3 - AutoBin files

         In transferring text files, the complete file is read
         sequentially and transmitted to the other station. However
         certain control characters such as LF and EOF markers are
         ignored and not transmitted. In other words the file itself
         will be changed slightly. With a text file, however, this is
         relatively unimportant since it will be read by the receiving
         station with a text editor or word processor and these
         controls can be replaced as required.

         The transfer of files that cannot be changed presents
         somewhat of a different problem. Files that the receiving
         station will store to disk and later use, such as *.EXE files
         or GIF picture files must be received exactly. To do this the
         file must be sent as a binary file.

         The AutoBin transfer is a further extension of the binary
         file transfer. Here a small simple protocol will be used that
         can detect possible errors in the transfer of the binary
         file. This routine takes place between the sending and
         receiving station through the use of checksum data. This for
         of transfer testing is compatible with Turbo packet and SP.
         This form of data transfer, therefore, is only possible if
         the receiving station is using a terminal program that allows
         this checking, such as Turbo packet or SP.

         5.3 Saving a QSO to disk (Alt-S)
         An ongoing QSO can be saved to disk through different
         methods. If the Save-to-Disk (Capture to disk) feature is
         activated, you need only change the menu selection when the
         QSO has ended to close the session. Following is a short
         description of different storage methods.

         5.3.1 Textfile online
         Here the text, in the moment that it is received, is saved to
         disk as well as displayed on the screen. Only the text that
         appears after the capture feature is enabled will be stored.
         This will continue until the capture feature is turned off.
         Both received and sent text will be saved to disk.

         5.3.2 Printer online
         This storage method works exactly like the Save-to-Disk
         feature (Diskette/Festplatte online). The one difference is
         that you have addressed your printer and your sent text has a
         different attribute than your received text, exactly like it
         does for the output to your screen.



                                    Page 15










         Video of sent text is inverse to that of the received text.

         5.3.3 Storage of select text
         Here you may select a portion of the text from the text
         buffer to store. You may find that you want to store part of
         a message received from a BBS and did not turn the save
         feature on before reading the message. This way you can read
         a message and then decide if you want to keep the
         information. Only text may be stored in this manner since you
         are going to recall data from the text buffer. Keep in mind
         that if your text buffer is small, some data may be lost. For
         this reason, you should consider a relatively large text
         buffer for the channel which you will normally read BBS
         traffic from (approx 500 lines). large files, such as GIF
         pictures that are coded in a text format, should be saved
         from the online mode.

         5.3.4 AutoBin
         This function saves binary files with a small transfer
         protocol that is compatible with Turbo packet, SP and AHP
         (Automode). For more explanation, see para 5.2. When you want
         to receive a binary file from another station, you must first
         activate the binary file transfer option. This must be done
         before the other station begins sending the file.

         5.3.5 Code-autosave
         Code-autosave is a handy feature for saving 7plus and LCPlus
         encoded files. Saving these types of files is automatically
         organized by GP and requires no input from the user. GP will
         recognize all type of 7Plus and LCPlus files, including the
         .ERR and .COR files. This becomes very practical when a file
         is sent in parts. GP automatically selects the proper names
         for the files and requires no other input with the exception
         maybe of "r 10-20" and then you can go get a cup of tea while
         the system takes over. The operation of this function is
         relatively simple; as soon as a 7Plus header is recognized
         and a save has not been initiated, GP automatically goes to
         online saving and informs you through an information window.
         The received data will be saved until and EOF marker is
         received. The saved file then contains only the file date;
         header information is not saved. Activation/deactivation of
         this function is further discussed in para 10.

         5.4 Remote operations
         GP contains a number of remote commands that a connected
         station can use to pull information from your system. All
         remote commands must be preceded by two slashes (//) so that
         GP will interpret what follows the slashes as a command. It







                                    Page 16










         is possible for problems to develop when a connected station
         accidentally places // in the first line while using a
         mailbox. For this reason, it is best to disable the remote
         functions on any channel being used as a mailbox.

         The description of each command is further explained in the
         file "HELP.RXE". The program must always be in the same
         subdirectory as GP since it may be started with the command
         "//h". It may also be called form DOS as a normal program.
         Particular remote commands may be sent by the sysop to a
         connected station, the results being the same as if the
         connected station had entered the command. This is done by
         first pressing the <ESC> key. A window will appear and you
         need only enter the remote command. As example, to send the
         help file to a connected station, simply press " <ESC>//h"
         and the file will automatically be sent to the distant
         station.

         5.5 External programs
         With the remote command of "//RUN", a connecting station can
         start an external program from your system. The output of
         this program will go to the TNC instead of to your screen.
         Because the output is redirected, the program run must be a
         DOS standard program. Additionally the keyboard cannot
         require any keyboard entries. All required inputs must come
         from the program itself. As example, we can use the Pascal
         program "HELP.PAS". In the setup of the program, the same
         macros as used by *.GPI files are available. If external
         programs are written in Turbo Pascal V4.0/5.x/6.0, you must
         be aware that screen output cannot be used. This is because
         GP writes directly to the video RAM or makes calls from the
         BIOS and these do not follow DOS standard. On the original
         diskette, you will find a program which may be used as an
         external program called SYSINFO.EXE that gives a short
         overview of your system. Any external programs made available
         to remote stations must be filed in a separate directory and
         a path to that directory established in the configuration
         file. The command to establish this path is "ExternalDir =
         <path>".

         5.6 Split screen
         If during a QSO you should wish to monitor all traffic on
         frequency, the Alt-F8 key combination will divide the screen.
         The upper half of the screen will continue to display the QSO
         and the lower half will put you in the monitor screen. With
         key combinations Alt-F9 and ALT-F10 you can move the screen
         division line up and down. This is also possible by using the
         mouse. Place the mouse cursor on the division line, press the
         left button and move the mouse up or down to increase or
         decrease the window size as desired.

         5.7 Scroll lock
         To stop scrolling of the screen text, simply press


                                    Page 17










         the scroll-lock key. The scrolling will stop but the text
         buffer continues to fill. If you forget to press scroll lock
         off, it is possible to fill the text buffer to where no more
         data will be accepted and you will receive error messages.

         5.8 TNC commands
         To change TNC parameters, you need only press the <ESC> key.
         An input window will open, enter the TNC parameter to change
         and again press the <ESC> key. The window will close and the
         parameter will change.

         5.9 Log book
         At your choice, GP will assume automatic logbook recording.
         This is accomplished with the command "LOG = ON" in the
         configuration file.

         6. Using "TheBox" (DieBox) utilities
         The following utilities for BBS operations are only available
         when the BBS is running TheBox software. In Germany most
         BBS's are using this software. When you are not completely
         familiar with the BBS's operation, read the help file
         provided by that BBS.

         6.1 The TheBox (DieBox) check function
         TheBox BBS's offer the possibility to read only those
         messages that have been logged since you last entered the
         system. This is done with the "(C)heck" command. This list is
         always sent in a particular format and GP is written such
         that it will recognize this format and places this list in a
         special buffer. This buffer is coupled with a selection
         capability that will allow you to easily select those
         messages that you want to read. The selected messages are
         automatically assembled into one command and sent to the BBS.
         Then you need only sit and wait for the text to be sent to
         you. As soon as you have disconnected from the BBS, the list
         is automatically deleted from memory. Naturally this function
         works with only one BBS at a time. If you were connected to
         more than one BBS on different channels, the list of each BBS
         would be entered into the same buffer and again you would
         have errors. To use this function, follow these steps:
         1) Connect to the BBS
         2) Give the command "C"<Return> to the BBS.
         3) After all messages have been listed form the BBS, press
         the Alt-F1 keys and the check function menu will appear. Buy
         use of the cursor keys and space bar, select those messages
         that you want to receive. This step can be repeated until you
         have read all messages of interest. At your choice, the list
         presented can also be presented by title instead of number.

         6.2 The TheBox (DieBox) list functions
         The list function in principle is the same as the check




                                    Page 18










         function. The difference being that the list function works
         only with one title at a time. It will search the BBS for all
         messages under the same heading and provide a list thereof.
         To use this function, follow these steps:
         1) Connect to the BBS
         2) Select a subject to search for, ie "L IBM"
         3) After all messages under this title have been sent, press
         the Alt-F2 key to get the list function menu. With the cursor
         keys and space bar, select those messages that you wish to
         read and hit <Enter>.

         7. The GP editor

         With the built-in editor, you have a simple text editor
         capable of working with small text files, such as the
         configuration file or info text files like "NEWS.GPI" or
         "CTEXT.GPI". The editor is a WYSIWYG with no fancy options.
         The advantage to  using the built-in editor is that you do
         not have to leave GP to edit a file. The size of the editor
         buffer is set in the configuration file. The buffer consists
         of 80 bytes per line. The minimum number of lines is 40 and
         the maximum 795 (approx 64K). There are two modes from which
         the editor can operate. These are the insert or overwrite and
         are controlled by the <INSERT> key. In the insert mode, the
         cursor will be half height compared to its normal size.

         In using the editor, you must understand the difference
         between screen lines (what appears on your monitor) and text
         lines (those sent to the buffer). Your screen displays a
         maximum of 80 characters per line. However the editor can
         work with a maximum of 255 characters per line. In any case
         should you exceed the maximum of 80 characters on a screen
         line (while in the insert mode) all the characters thereafter
         will be ignored. The end of a line of text will be marked
         with a bracket. If the bracket is missing, then the next line
         of text will be sent to the buffer without a CR/LF appearing
         on the screen.

         To load a file to be edited, press the Alt-L keys and then
         enter the name of the file.

         To save a file after editing, press the Alt-S keys and enter
         a name for the file to be saved.

         To create a new file, press the Alt-L keys and give the name
         of the file to be created. The system will ask if new file
         should be created. Reply with "J" (German 'Ja').

         8. The MH list (Alt-H)
         GP keeps an MH list which lists the last 40 stations





                                    Page 19










         heard. This list can be viewed with the command //MHeard sent
         by the distant station. The MH list is constructed from
         callsigns heard on the monitoring channel and is continuously
         updated. The monitor mode should not be set to "N" or the MH
         function will have no entries. The MH list offers the
         possibility of checking whether a heard station (callsign)
         exists in the NAMES.GP file. To check, simply move the cursor
         line over the callsign and press <Enter>. The selection can
         be made with the cursor keys or the mouse.

         9. The autorouter
         The autorouter within GP allows you to connect to known
         stations without having to enter the entire connecting path
         (vias). The only restriction is that the known station
         information must exist in the NAMES.GP file. The list entries
         always have the following syntax:

         TYPE>CALLSIGN NAME; PATH

         It is very important that the type be entered correctly, as
         this information tells GP what actions must be performed and
         what actions are unnecessary. The NAME of the station can be
         as long as you like, but the program recognizes the first 22
         characters of the NAME. If a station can be connected to
         direct (no vias) then the path is simply left off. Otherwise
         the path contains a list of all the necessary digipeaters. A
         digipeater entry will always have the following syntax:
         TYPE>CALL.
         The TYPE can be entered as the following letters:
         B  : Mailbox
         D  : Digipeater
         F  : Flexnet digipeater
         N  : Netrom or Thenet digipeater
         T  : End station
              (Should an end station be used as a digipeater, GP
               automatically generates a "//C..." command.)

         With these types, GP recognizes the format required to
         connect to, or through, each station to the final
         destination. An entry in the NAMES.GP would look like the
         following:

         T>WB0UPX Mike; N>#TR440 N>HBK N>BEL N>VB N>THR T>WB0UPX

         In this case, GP would connect to the first node and the
         request a connect to each subsequent node and finally a
         connect request to WB0UPX.

         An entry in the names list that requires digipeating would
         look like the following:

         T>WB0UPX Mike; D>KA4P N>#TR440 N>HBK D>BEL D>VB D>THR
                        T>WB0UPX


                                    Page 20










         In this case upon a connect request, GP would try and connect
         to #TR440 via KA4P, using KA4P as a digipeater. Likewise
         through BEL, VB, and THR.

         9.1 Recursive paths
         It is not necessary to list the entire path for each station.
         When GP knows the path to one station and that station
         appears in the path of a second station, GP will
         automatically build the path to the second station. As an
         example:

         F>DB0FN Digi Siegen
         F>DB0WST NetNode West; F>DB0FN F>DB0WST
         F>DB0ME-3 Digi Sollingen; F>DB0WST N>DB0ME-3
         B>DB0SGL BBS Siegen; F>DB0FN B>DB0SGL
         B>DB0IZ BBS Sollingen; N>DB0ME-3 B>DB0IZ

         Because the path to DB0ME-3 established the path through
         DB0WST, it is not necessary to enter the same info in the
         file for DB0IZ. By entering on DB0ME-3 in the path for DB0IZ,
         GP automatically routes traffic through DB0WST and then to
         DB0ME-3 and finally to DB0IZ.

         The use of recursive paths has two advantages:
         1) You have to type less
         2) It allows more flexibility in the event that a specific
         digipeater or node drops and a new link has to be
         established. The changes are then required to only one entry
         in the file. All other entries using that path automatically
         assume that route.

         9.2 Routing through SP gateways
         Should it be necessary to establish a path that has an SP
         gateway station in it, in which a port number must be given,
         there is trick to this and that is through the use of a
         "dummy digi". As an example:

         DL9ZZZ is an SP-gateway. He has two ports, Port0 on 70 cm and
         Port1 on 2 meters. Station A is operating on 2 meters and
         wishes to connect to DB0XYZ on 70 cm. The connect command
         must be sent then as "//C DB0XYZ 0". The path entered into
         NAMES.GP would be as follows:

         N>DB0XYZ Testdigi; T>DL9ZZZ D>0 N>DB0XYZ

         GP would first connect to DL9ZZZ and then send the command
         "//C DB0XYZ 0". This trick works not only with SP gateways,
         but also Baycom Nodes, when a port number must be given.

         10. Setup (Alt-U)
         GP offers the possibility of changing many of the program
         parameters. These include changing colors, activating or
         deactivating remote operations for particular channels, etc.
         The individual menu options may be selected with

                                    Page 21










         either cursor functions or a mouse. Upon exiting GP (Alt-X),
         all of the existing parameters are stored in the file
         CSTAT.GP and then reloaded at the next start of the program.
         Each channel has its own setup menu. These menus for the
         mailbox utilities, the editor, the MH list and the monitor
         are not so ?????????  as is the case with the QSO channels.

         10.1 Changing colors
         After you have entered the menu for changing colors, move the
         select bar on one of the three attributes, and with the
         cursor-left or cursor-right keys, select the new color. The
         selected color will appear in a small window. If this color
         is the one you have selected, go to the menu and hit
         "Accepted changed color" (Geanderte Farben Ubernahmen).
         Should you decide not to change the existing colors, you can
         exit the menu at any time by pressing the <ESC> key. If you
         want the selected colors to be a permanent, you must make the
         changes to the configuration file.

         10.2 Remote operation prompt
         The remote operation prompt is fixed in the program and will
         allow remote operation of your station by a connecting
         station. The prompt for remote operations will only be sent
         to the connecting station by remote entry of the command
         //Prompt = ON. The prompt can include any or all of the 9
         possible macros exactly as with the *.GPI files. The prompt
         feature is available for all available channels.

         10.3 Remote operation activation/deactivation
         The menu selection "Remote control" (Fernsteurung) shows the
         actual status of remote operations. To activate or deactivate
         this feature, simply click (or press <RETURN>) this menu
         selection. The activation/deactivation applies only to the
         current channel selected.

         10.4 Text buffer backup
         This menu feature (TextBuffer-backup) serves to turn off the
         backup function. This state of this function, unlike the
         others, is not stored in memory. Upon a restart of GP, the
         program will accept the status of this function as defined in
         the configuration file.

         10.5 Echo
         This selection turns ON/OFF the local echo to screen. In the
         ON state, text to be sent will be echoed to the screen. In
         the OFF state, only received packets are displayed on the
         screen. The command applies only to the selected channel.

         10.6 RX-click
         With the features of RX-Click, you have the option of an
         audible alarm to signal when you have unread packets




                                    Page 22










         received but not read. Additionally you may specify if the
         alarm function applies to only unmonitored channels or to all
         channels. The parameter values for this function are:

         0 : No audible signal for any channel
         1 : Audible signal for those channels not currently
             displayed
         2 : Audible signal for all channels

         10.7 Line length (zeilenumbruch)
         This parameter sets the maximum number of characters
         allowed per line. In CONVERS mode this should normally be set
         for 65 characters per line. This parameter applies only to
         the current selected channel.

         10.8 Packet length
         This parameter establishes the maximum number of characters
         that an ax.25 packet may contain (PACLEN). This parameter
         applies to all channels.

         10.9 Soft scroll
         This turns the soft scroll function ON/OFF. See para 14 for
         more information.

         10.10 Code autosave
         This feature turns the autosave function for 7Plus and LCPlus
         files ON/OFF. This feature applies to all channels. For more
         information see para 5.3.5.

         11 DOS shell
         Through this feature you have the possibility to execute DOS
         commands without leaving GP. To return from DOS to GP, enter
         the command "EXIT" <ENTER>. In the configuration file
         (CONGIF.GP) you should have an entry "TNCDOS = M N". If not,
         you stand the chance of running out of memory as the TNC
         buffer continues to receive packets.

         12. Using a mouse
         If a mouse is connected to the computer and a driver is
         already loaded, GP will automatically recognize this fact and
         allow full use of the mouse with icons and menu selections.
         Use of the mouse is straightforward. Simply move the mouse
         cursor to the icon or menu selection and "click" the left
         mouse button. Press the mouse button until an audible signal
         is heard. Because of variations in video systems, some
         systems may require that you hold this button down longer
         than others. Should you inadvertently select an option by
         mistake, simply move the mouse cursor outside the selection
         field and "click". This will return you to a normal screen.
         The mouse functions exactly the same in using the check or
         list functions. Move the mouse to the scroll bar, and holding
         the left button pressed, move the mouse/scroll bar over the
         desired option. Release the left button and press


                                    Page 23











         the right button to select this option (has same effect as
         pressing the space bar).

         12.1 The scroll bar
         In all the text windows you will find a scroll bar on the
         right border of the monitor screen. With this bar you have
         the possibility to scroll forwards or backwards or sideways
         through the entire scrollback buffer. To scroll multiple
         lines, it is necessary to "click" both displayed arrows. To
         view an entire screen, you must only "click" the cyan colored
         area either above or below the scroll bar. To go to a
         specific position in the buffer, you need only "click" on the
         scroll bar and, holding the mouse button down, move up or
         down through the text.

         13. Command line parameters
         GP will accept certain command line parameters at start-up
         which will affect the operation of the program.

         13.1 "/e" and "/v" commands
         These commands force GP to start either in EGA or VGA mode
         and ignore the parameter specified in the configuration file.
         Example:

         "GP /e" (or GP286 /e) starts GP in the EGA mode (640X350)
         "GP /v" (or GP286 /v) starts GP in the VGA mode (640X480)

         13.2 "/h" command
         Upon initialization, if GP finds that your tnc is currently
         in the host mode, you would normally get the error message
         "TNC not in Terminal Mode". GP would interpret this message
         to indicate that either the software running was not
         compatible or the baud rate of the TNC was different than
         that established by GP. With the "/h" parameter, GP is told
         that the TNC is already in the host mode and the program will
         not try to force host mode switching of the TNC. Should there
         actually be a baud rate error, or problem with the TNC, GP
         will close itself.

         14. Soft scroll
         One feature of GP is choice of switching text scrolling from
         normal scrolling to software controlled scrolling. Soft
         scrolling means that instead of 8 - 16 lines at one time, 4 -
         8 lines are scrolled up. This gives a much smoother "roll"
         to the lines. The one disadvantage to soft scrolling is that
         it is slower. The other problem with soft scrolling is
         associated with some VGA cards, an in particular with super
         VGA cards. Should a problem develop, such as loss of on
         screen text, you can enter the DOS shell and the type "EXIT"
         to return to GP. This should reset the screen. While the
         screen is restoring, press Alt-U keys and go into the setup
         menu and turn soft scrolling off.


                                    Page 24











         15. What is host mode on the TNC2?
         Surely you have wondered what host mode is when referred to
         by a terminal program.  Host mode is mode of the TNC2 that
         handles data transfer between the computer and the TNC in a
         completely different manner than a normal terminal program.
         In this mode the terminal program (in the computer) acts as
         the host and the TNC acts as the slave, which means that the
         TNC sends no data to the terminal program until the term
         program sends the command to do so. Under this method,
         theoretically, it is guaranteed that data will always flow to
         the channel intended. In operation, the terminal program
         sends in order, a query to each tnc channel asking if data is
         waiting or not. If there is data waiting, then the TNC sends
         this to the terminal program. Because of this method, it
         takes a few seconds before data received by a channel appears
         on the monitor screen. GP itself cannot determine when there
         is data waiting on a channel and it must also constantly
         query each channel. While this is happening, GP is performing
         other functions also, such as text input from you. This also
         takes time. During this constant transfer of data, should an
         error transpire, GP will recognize it immediately and attempt
         to clear the error with the TNC. You will be notified in a
         window on the screen that an error has occurred
         (synchronization error).

         Host mode cannot be changed directly with ax.25 protocol. The
         TNC acts as an intermediate storage device that receives
         ax.25 protocol data from your radio, changes the format and
         then stores it until queried by the terminal program.
         Conversely, it accepts data from the terminal program,
         converts this to ax.25 protocol data and waits to transmit
         this to your radio.

         There are certain things that the terminal program has no
         control over, such as the number of retires. For these
         things, the terminal program can only query the TNC as to
         status and display the information, nothing more.

         Host mode was developed specifically for "intelligent"
         terminal programs with multiconnect capabilities and
         incompatible with 'normal' terminal programs.

         Unfortunately, there are a number of TNC softwares, TAPR
         software for example, which cannot implement Host Mode. Only
         the WA8DED software and the Firmware (NORD><LINK) have
         implemented this mode. This is the reason that programs such
         as GP, SP, THP, etc will only work in conjunction with this
         TNC software.

         In the meantime, there are programs that will allow the TNC
         to function with other than The Firmware. One of these, for
         example, is DL1MEN's TFPCR. This program offers a KISS-HOST
         interface for use with TAPR-Software.

                                    Page 25











         Another program is TFPCX by Y51GE, which replaces the entire
         TNC and requires only a simple modem between computer and
         radio. GP works equally well with either program.

         16. Synchronization errors
         Synch errors between the TNC and terminal program happen
         whenever one or more characters are lost or changed during
         data transfers. Should this happen, GP will attempt to bring
         the TNC back to a stable state. Should GP not be able to
         resynch with the TNC, the program will end and the computer
         return to DOS. It is possible that because of a power loss,
         for example, GP is unable to restore any communications with
         the TNC. For this reason, an "emergency brake" has been built
         in that stops the attempts to resynch and presents a menu on
         the screen. This menu will give you control over further
         attempts by GP to reestablish communications with the TNC or
         not. In this way, you may be able to reset your TNC and
         resume communications without having to leave GP. This is
         done by selecting the "TNC re-initialize" option.

         If using TFPCX or TFPCR, a resynching problem should never
         appear.

         17. Tips
         To close, a few more tips in using GP.

         It would be in your best interest to identify a specific
         channel for BBS or mailbox QSO's. Because of memory
         limitations, you obviously cannot reserve a large buffer area
         for each channel. It is recommended that you make the last
         channel (Channel 4 for a 4 channel system) your "mailbox"
         channel and set the buffer area for this channel as the
         largest one. The reason for using the last channel in the
         system is that all other channels would have to be in use
         before this channel can be connected to by other stations.
         This way, you are always insured of having a free channel to
         connect to your local BBS/Mailbox. Another reason is because
         of remote operations. This function can be turned on/off
         for each channel individually. For the mailbox channel, you
         should always turn the remote control feature OFF. This is
         because in certain messages received, control characters
         could exist to which GP would react. This could do
         irreversible damage to your files or programs.

         GP differs from other terminal programs in that it does not
         function in TEXT mode, but in GRAPHIC mode. The advantage to
         this is the flexibility in layout and display features, but
         the drawback is that GP must work with a much larger video
         memory area. This explains why the screen output from GP may
         be slower than other terminal programs. If you have shadow
         RAM capability within your computer, you can overcome most of



                                    Page 26











         the speed loss. This also accounts for the somewhat slower
         response to your mouse by GP. The loss of some speed also
         accounts for having to wait until a current line of text is
         fully displayed before being able to change from one channel
         to another.

         Test Mode:
         If you wish to start GP without a TNC connected, simply use
         the "/h" command at start up (see para 13.2). GP will inform
         you of a synch error and you must then only hit Ctrl-Break
         and select the "Ignore TNC" option on the menu list.
         Obviously in this mode, no QSO's are possible but the editor
         is fully functional. This trick will not work if using either
         TFPCR or TFPCX.

         Should you receive the message "TNC not answering" upon
         start up, there is no reason to panic. In this case, just
         reset the system and try again. Should the system still not
         come up after the second try, it is possible that the TNC is
         already in the host mode. In this case, simply start GP with
         the "gp /h" command. If after trying all of the above, you
         still receive a resynch error message, look at the following:

          - The serial port specified in the config file is not the
         port your TNC is using.
          - The baudrate in the config file is wrong.
          - The IRQ of the serial port specified in the config file is
          not correct.
          - The serial cable between computer and TNC is bad.
          - The TNC is not functioning properly. Try a TNC reset.


         Translated from documentation dated 9 Feb 92.
         Not responsible for errors or misrepresentations.

         Transcribed from hardcopy to disk 6 May 93.